S1
D7
S2
D8
S3
D9

L1

D2
L2

D3
L3

D4
L4

D5
L5

D6

GPIO	Device	Function	Variable
-	Internal LED	loop running
D2	L1 (blue)	Device on	LED_ON
D3	L2 (green)	(blink) Auto-Buzzer	LED_AUTOBUZZ
D4	L3 (yellow)	(on) External bell active / (blink) Door Buzzer active	LED_EXTBELL_BUZZER
D5	L4 (red)	Error	LED_ERROR
D6	L5 (white)	(blink) Door Ring detected	LED_DOORBELL
D7	S1	Switch Auto Buzzer Mode	SWITCH_BUZZMODE
D8	S2	Test Ring (External Gong + MQTT)	SWITCH_TESTBUZZ
D9	S3	Test Buzzer	SWITCH_TESTRING
D10		Input Bell	INP_BELL
D11	Rel1	Output Buzzer	RELAIS_BUZZER
D12	Rel2	Output External Bell	RELAIS_EXT_BELL

Arduino
Relais 1
Relais 2
LEDs L1-L5
Switches S1-S3

External Bell
(Remote)

House Intercom
Bell Signal
 (AM 40)
Door Buzzer
Button

External Bell
(Remote Control)
External Bell
Broker
PC
Client

WLAN
proprietary protocol